## Slide 1: TENORM Study Update Presented by Rich Janati on behalf of Dave Allard
Low-Level Waste Forum Meeting
October 2014

## Slide 2: Background
Technologically Enhanced Naturally Occurring Radioactive Material
  TENORM, a naturally occurring radioactive material not subject to regulation under the laws of the Commonwealth or the Atomic Energy Act of 1954, whose radionuclide concentrations or potential for human exposure have been increased above levels encountered in the natural state by human activities.
  PA DEP Regulations, Title 25, Chapter 271

## Slide 3: NORM

## Slide 4: Background
Generation of TENORM has increased significantly. This is mainly due to the recent expansion in natural gas exploration and production in Pennsylvania within Marcellus Shale formation.
There are many issues with TENORM
that must be managed effectively.
These issues include:
Potential Worker Radiation Exposure
Possible Public Radiation Exposure
Environmental Contamination (soil, water, etc.)
Waste Disposal

## Slide 5: Marcellus Shale

## Slide 6: Marcellus Shale - Rad. Data
MS uranium content: 10-100 ppm
MS U-238 content: 3.4 - 34 pCi/g
MS Ra-226 content: 3.4 - 34 pCi/g
MS frac water Ra-226: 300 - 9,000 pCi/L
Treated frac water sludge: 6 - 250 mR/h

## Slide 7: Solid Waste Radiation Monitoring
PA DEP Requires Radiation Monitoring at all PA landfills.

## Slide 8: Rad Monitors at All PA Landfills
PA has only RCRA D landfills for non-haz waste
Alarms set at 10 uR/h over background
Rad Protection Actions Plans require an evaluation of solid waste to determine cause
Most is waste contaminated with medical radionuclides (e.g., I-131, Tc-99m)
Have always seen TENORM waste sent for disposal from ‘conventional O&G wells’
Increase from unconventional wells

## Slide 9: Well Types

## Slide 10: Natural Gas

## Slide 11: Site Categories for Sampling
Waste water treatment plants (WWTPs)
Landfills
Waste sludge loads to landfills
Well pads
Underground natural gas storage sites
    Gas-fired electricity generating facilities
Compressor stations
Beneficial use sites
Decommissioned well casings

## Slide 12: Sample Types
Natural gas samples
Liquid samples (i.e., frac, flowback and produced water)
Solid samples (i.e., drill cuttings, sludge, soil and sediment)
Radiation surveys
‘Swipe’ samples

## Slide 13: Sample Analysis
The samples are being analyzed for the presence of alpha, beta and gamma radiation (gross counting and spectroscopy).
The gas is being sampled for the presence of radon-222.

## Slide 14: Work Completed in 2013
184 Site visits
114 Locations
1,000 Samples analyzed
25 WWTPs / 73 visits (3 rounds)
48 Landfills
Evaluating the effect of waste sludge
transport on external radiation levels

## Slide 15: Work Completed in 2013
20 Well pads / 41 visits
13 Beneficial use sites
1 Decommissioned well casings disposal site
7 Facilities that compress, store and utilize natural gas

## Slide 16: Field Work in 2014
Well pad sampling (23 visits to 11 pads)
Continued landfill leachate collection (5 facilities)
Landfill ‘bulking’ operations (2 facilities)
Beneficial use sites (4 sites)
Gas-fired power plants (1 facility)
Gas storage facilities (4 facilities)

## Slide 17: Field Work in 2014
Compressor stations (1 facility)
Gas processing facilities (1 facility)
Wastewater impoundments (2 facilities)
Evaluating the effect of transport on sludge external radiation levels (5 events)

## Slide 18: Field Work in 2014
Landfills – recovered deployed radon detectors (8 facilities)
• Landfills – waste bulking (2 facilities)
• Well Pad – completed, 1 production phase gas collection for radon
Well Pads – ambient gamma surveys of areas with buried rock cuttings

## Slide 19: Field Work - Locations

## Slide 20: Field Work
Radon testing
at a gas storage
facility

## Slide 21: Field Work
Radon testing
at a gas power
facility

## Slide 22: Field Work
Flow-back
sampling
at a well
pad

## Slide 23: TENORM Waste Issues
Results of sludge and rock cuttings being evaluated
Samples were counted by gamma spec for Ra-226 and Ra-228
ICP-MS and neutron activation performed on rock cutting samples
Data will inform any needed updates in approach for TENORM disposal
ICP-MS: Inductively Coupled Plasma Mass Spectrometry

## Slide 24: Schedule
Field work has been completed as of August
Sample analysis, data analysis and report preparation from March through fall 2014
Internal DEP final review now on-going
Peer review fall 2014
Final study report planned for completion in 2014.

## Slide 25: TENORM Study Information
Study-related documents are available at www.dep.state.pa.us Keyword “TENORM”
Updates are being provided to various stakeholders