## Slide 1: Department of Energy Office of Waste Management Update
Doug Tonkay
Director, Office of Disposal Operations
Low-Level Radioactive Waste Forum, Inc.
October 22, 2015

## Slide 2
  Update on Waste Isolation Pilot Plant (WIPP)
  Update on low-level radioactive waste (LLW) and mixed LLW (MLLW) waste disposal at DOE facilities
  Waste management forecasts
  Manifest Information Management System (MIMS) update
  Other departmental highlights and activities
Presentation Topics

## Slide 3: WIPP: Key Recovery Steps
  Documented Safety Analysis revisions
  Safety Management Program revitalization
  Underground restoration
  Re-establish degraded equipment
  Fire protection
  Maintenance and ground control
  Radiological risk mitigation
  Soot cleaning of electrical panels
  Expedited mine stability
  Initial Panel 6 and Panel 7, Room 7 closure
  Interim ventilation and supplemental ventilation modifications
Notes: Background on Incidents:
Fire:
Occurred shortly after 11 a.m. on Feb. 5.
86 people in the mine, all exited safely; 6 personnel were transported to the Carlsbad Medical Center for smoke inhalation were released the same day. 7 were treated on-site.
WIPP’s Emergency Operations Center was activated.
An underground vehicle used to transport salt was on fire in the underground.
All operations at the repository ceased at that time.
Radiological Incident:
Shortly before midnight on Feb. 14 a continuous air monitor detected a radiological release in the underground.
HEPA filters on-site immediately engaged, thereby minimized releases to the environment.
Monitors on site detected slightly elevated levels of airborne radioactive concentrations, which is consistent with the type of radiation TRU waste has when being placed in the repository.
After recognizing that it wasn’t a radon event, additional precautions were taken to shelter workers.
Concentrations were then and remain today well below a level of public or environmental hazard.
Samples from around the site have been taken and results are confirming these findings.
22 workers on site Feb. 14 and Feb. 15 were exposed to extremely low levels of americium and plutonium these employees are unlikely to experience any health effects as a result .

## Slide 4: WIPP: Areas of Significant Progress
  Ground control – 85% of catch-up bolting complete
  Radiological risk reduction – over 65% of underground released as controlled area
  Soot cleaning – 98% complete
  Zone recovery (Zones 1-7) – complete
  Initial closure of Panel 6 and Panel 7, Room 7 – complete
  Revision of DSA in progress
  Interim Ventilation System (IVS) – repairs completed, proceeding with installation
  Supplemental Ventilation System – complete, waiting for IVS (must be operated in tandem)
  Hybrid diesel electric bolter in operation – training ongoing
  Approval of Integrated Performance Measurement Baseline – in progress

## Slide 5: WIPP: AIB Reports and Corrective Action Plans
  CBFO/NWP Corrective Action Plans (CAPs) for judgments of need (JON) from Accident Investigation Board (AIB) reports on haul truck fire and Phase I radiological event approved in February 2015 – now in implementation
  AIB Report for Radiological Release Event, Phase II, issued April 2015
  Phase II focused on determining direct cause of release
  Phase II CAPs approved in early September 2015 – now in implementation

## Slide 6: TRU Waste Generator Impacts
  Prioritization of shipments
  Premature at this stage of recovery to predict and allocate rate of TRU waste shipments to WIPP
  Initial focus will be on emplacement of wastes generated during recovery activities and emplacement of wastes currently stored in WIPP surface facilities (wastes were received but not emplaced prior to the events)
  In determining rate of shipments among sites, DOE will consider numerous technical and programmatic factors
  WIPP transportation and waste acceptance capabilities
  Generator site compliance commitments
  Storage capacities
  Construction of additional surface storage at WIPP is one option under consideration

## Slide 7: WIPP Way Ahead
  Develop new PMB based on current schedule/cost impacts
  Complete installation and testing of interim and supplemental ventilation
  Complete Documented Safety Analysis, Contractor Management Assessments, Operational Readiness Reviews
  Resume waste emplacement

## Slide 8: DOE’s Unique Waste Management Mission
  Authority and responsibility for management of all DOE-generated waste under authority of the Atomic Energy Act, as amended
  DOE has unique waste streams because of its historic and present missions
  Clear distinction between DOE and non-DOE waste in the Low-Level Waste Policy Amendments Act
  State and regional disposal compacts responsible for disposal of non-DOE and non-naval decommissioning LLW
  DOE does not accept LLW/MLLW from non-DOE generators unless there is documented DOE nexus or national security rationale in accordance with eligibility criteria

## Slide 9: DOE LLW/MLLW Management Policy
  DOE Order 435.1, Radioactive Waste Management, with associated guidance, provides policy and requirements for DOE Waste Management
  Current LLW disposal policy:
  Dispose of radioactive waste at site where generated, if available
  If disposal is not available on-site, then off-site at another DOE facility
  Disposal at a non-DOE facility when compliant and protective of health and safety and in the best interest of the government
  Exemption documentation includes annual facility reviews, life-cycle cost analysis, etc.
  Historically, DOE on-site (~90% by volume), DOE off-site (~5% by volume), and commercial disposal (~5% by volume)
  DOE generally does not utilize State compact facilities for disposal of LLW/MLLW

## Slide 10
Chart: Millions of Cubic Feet
| FY12 Actual | FY13 Actual | FY14 Actual | FY15 | FY16 | FY17
OnSite | 32.5252 | 19.1627 | 22.9919 | 11.1813 | 2.7928 | 3.3174
Commercial | 0.34697 | 0.92406 | 0.55806 | 1.4384 | 0.48807 | 0.29966
NNSS | 0.67268 | 1.0109 | 1.27 | 1.2979 | 1.5 | 1.5
TBD | 3.1911e-05 | 0.0081084 | 0.004176 | 0.010231 | 0.010323 | 0.17655
Complex-wide LLW/MLLW Disposal
by Location

## Slide 11: FY15 NNSS Disposal Volumes
    Forecasting supports operational planning
    Updated quarterly
Generator Site |  | FY15 Actual* (ft3) | FY15 Actuals + Remaining Forecast for Sep 2015 (ft3)
Portsmouth GDP (OH) |  | 543,827 | 627,918
Oak Ridge Reservation (TN) |  | 126,540 | 164,507
Oak Ridge NNSA/Y-12 (TN) |  | 118,422 | 130,672
Los Alamos National Lab (NM) |  | 33,282 | 52,861
Idaho Site (ID) |  | 125,916 | 138,122
Livermore Nat'l Lab (CA) |  | 45,684 | 48,572
Paducah GDP (KY) |  | 5,465 | 5,465
NNSA/Nuclear Fuel Services (TN) |  | 39,506 | 47,001
Onsite NNSS (NV) |  | 13,348 | 13,348
Savannah River (SC) |  | 535 | 1,075
Berkeley |  | 0 | 0
West Valley (NY) |  | 9,078 | 9,078
All other sites |  | 57,281 | 66,245
Total |  | 1,118,884 | 1,304,864
    * Actual volumes thru 8/23/15

## Slide 12: DOE LLW/MLLW Forecasts
  EM updates its DOE-wide life-cycle LLW/MLLW forecasts annually in coordination with other Program Offices – NNSA, SC, NE, and Naval Reactors
  Information publicly available through Waste Information Management System (WIMS) maintained by Florida International University

## Slide 13: Manifest Information Management System
  DOE maintains Manifest Information Management System (MIMS) under requirement of the LLWPAA (since 1986)
  System updated to meet current DOE IT platform requirements
  Update ongoing to add search capability by “generator identification number”
  Hosted at: http://mims.doe.gov/
  Provides LLW disposal manifest volume and activity information with generator class as provided by disposal site (does not identify specific generator)
  Currently, system has records from operating disposal sites at Barnwell, SC; Clive, UT; Richland, WA; Andrews, TX; closed Beatty site
  Barnwell (Chem-Nuclear): 1986-2014
  Clive (EnergySolutions): 1992-2014
  Richland (US Ecology): 1986-2014
  Andrews (WCS): 2012-2014

## Slide 14: Current MIMS Status
  New user-defined reports now available with both volume and activity breakout by classes (replacing old standard reports)
  Ongoing collection of 2015 data
  Continuing to make improvements based on user feedback, such as capability to search by generator
  Industry has requested NRC allow waste generators to cite MIMS data for solid radioactive waste disposal in lieu of creating redundant reports to meet annual Radioactive Effluent report requirements (RG 1.21)

## Slide 15: Other Waste Management Updates
  Final GTCC EIS undergoing internal review; expected publication next quarter
  EM currently working to resolve comments on DOE Order 435.1
  DOE anticipates DOE-wide review early next year
  EM anticipates public comment and formal REVCOM review next year
  National Environmental Policy Act documentation initiated for location(s) to dispose of depleted uranium oxide conversion products generated from DOE's inventory of depleted uranium hexafluoride
  Maintenance of corporate programs to integrate waste disposition efforts (such as LLW and TRU Corporate Boards)
  Recurring forums for discussion and problem-solving with contractors, i.e. EFCOG Waste Management Working Group

## Slide 16
BUILD
&
TREAT
EXCAVATE
DEMOLISH
SAFEGUARD
TRANSPORT
PACKAGE
Questions
SAFEGUARD