## Slide 1: EPRI Development of Nuclear Power Plant Implementation Guide for NRC Branch Technical Position on Concentration Averaging and Encapsulation
Presented by Karen Kim, Sr. Technical Lead, EPRI on behalf of Mike Snyder, Sr. Technical Lead, EPRI
LOW-LEVEL RADIOACTIVE WASTE FORUM, INC.
Fall 2015 Meeting
Chicago, Illinois
October 22-23, 2015

## Slide 2: Project Objectives
Create an Implementation Guide for the Branch Technical Position on Concentration Averaging and Encapsulation, Revision 1
  Specifically for nuclear power plant wastes.
  Common Understanding of Key Concepts
    Averaging Constraints
    Hot Spots
    Waste Streams and Types
    Characterization and classification
    Discrete Items
    Blending
    Encapsulation and Solidification
  Consistent Implementation
  Reliable Acceptance and Enforcement

## Slide 3: EPRI LLW R&D: Three Prong Strategy
Waste Minimization
Disposal Flexibility
Class A Minimization
Class B/C (ILW) Minimization
Global Profiles
Storage Facility Operating Guidelines
Waste Containers
Waste Forms
Facility Design
Safe Storage
10CFR61 (US Waste Disposal Regulation)
BTP Revision & Implementation Guidance
VLLW
International Waste Characterization
Liquid Waste Processing
Generate Less, Store Safely, Facilitate Disposal
BTP = Branch Technical Position on Concentration Averaging
Notes: approach – first don’t generate, second what you do generate if there isn’t disposal – then safely store it (no events) and finally, improve regulatory framework to get more into the disposal site at a lower cost. The following slides will let you go into deeper discussion about each of the areas. Strategic rather than reactive

## Slide 4: Facilitate Disposal
Disposal Flexibility
Global Profiles
10CFR61
BTP Revision & Implementation Guidance
VLLW
International Waste Characterization
Objective: Produce a sound technical basis to more accurately assess the hazard and risk associated with LLW
Use this information to inform discussions related to regulatory changes
Maintain disposal safety
Potentially increase disposal flexibility
Notes: approach – first don’t generate, second what you do generate if there isn’t disposal – then safely store it (no events) and finally, improve regulatory framework to get more into the disposal site at a lower cost. The following slides will let you go into deeper discussion about each of the areas. Strategic rather than reactive

## Slide 5: Review of Project History
2005 ACNW Issues White Paper on the Need for an Updated Framework for LLW
2006 EPRI Begins Investigating Bases and Technical Options
2007 NRC Strategic Assessment Opens the Door
2007-2012 EPRI Research Identifies Opportunities for Regulatory Change and Supports BTP Revision (EPRI Report 1021098)
2012 Draft BTP Revision 1 Issued by NRC (May)
2012 EPRI Research and Comments (EPRI Report 1025302)
2015 BTP Revision 1 Issued by NRC (February)
Notes: Phung will provide edits to this slide. We started on this work before 2007…
ACNW= Advisory Committee on Nuclear Waste

## Slide 6: Revision of BTP and EPRI Project Role
Revision 1 of the BTP:
  NRC’s intention was clarification
    New BTP should mean what it says
  NRC recognized existing methods and tried to accommodate them
  Explanations in the BTP revision also clarify the positions in the 1995 BTP CA (which is still applicable).
EPRI Project’s Role:
  Bring together various stakeholders’ perspectives of the BTP, as it is written, and document a common understanding and interpretation of the BTP to develop an Implementation Guide for nuclear power plant wastes.
Development Supported by Working Group:
  Utility and industry shipping subject matter experts, representatives from disposal sites, representatives of disposal site state regulatory bodies, representatives of the NRC
Notes: Focus on our role is to take this new document (which is great) and provide additional clarification. It is not our job to re-write, change, or alter the interpretations. It’s a recognition that each organization on this group has different perspectives. Bring together Develop a common interpretations of the paragraphs.

## Slide 7: Topics Addressed in BTP
Provide Guidance and Examples for
  Blending of Resins and other wastes
  Solidification of shredded filters
  Justification for Treatment of Cartridge Filters as Blendable
  Concentration Averaging of Discrete Items
Averaging now with respect to Class limits rather than container average
Notes: NOTE – still working on discrete sections
Blendable waste would typically be applied to the following Uniform Manifest Waste Stream Codes:
20, Charcoal
21, Incinerator Ash
22, Soil
26, Filter Media
27, Mechanical Filter (with restrictions)
30,Cation Ion Exchange Media
31 Anion Ion Exchange Media
32 Mixed Bed Ion Exchange Media
35, Glassware or Lab-ware (with restrictions)
38, Evaporator Bottoms/Sludges/Concentrates
39, Compactible Trash (with restrictions)
40 Non-compactible Trash (with restrictions)

## Slide 8: How It Works
High Activity Resin
CVCS/Crudburst/SFP/RWCU
Class B/C or ILW
(35 cft, 150 Ci)
Low Activity Resin
SGDB/Condensate/RW
Class A or VLLW/LLW
(55 cft, 10 Ci)
A
Volume = 90 cft
Activity =160 Ci

## Slide 9: Implementation Guidance Content
Describe what each chapter/section of the BTP means and how to implement it for each applicable waste stream.
Compare the new BTP guidance with the old, identifying what has changed and providing an analysis of the impact of this change.
Provide flow charts and examples
Evaluate alternative approaches discussed in the BTP; when they may be appropriate and what to consider.
Notes: Important Slide

## Slide 10: Deliverables
Draft Guidance Document (Spring 2015)
  Outline
  General Language
  Identification of Examples
  Working Group Provided comments and feedback
  Incorporated into draft
Currently collecting examples for analysis and inclusion into Implementation Guide
Working Group will reconvene on November 5 & 6
  Final review
  Goal is to vet the current draft content, examples and ensure all previous comments have been addressed to the satisfaction of the working group.
Final Report (Spring 2016)