## Slide 1: TENORM in Municipal Solid Waste Landfills: Assessing the Risk
Jim Grice, Radioactive Materials Unit Leader
James.Grice@state.co.us

## Slide 2: TENORM Defined
…naturally occurring radioactive material whose radionuclide concentrations are increased by or as a result of past or present human practices. TENORM does not include background radiation or the natural radioactivity of rocks or soils. TENORM does not include "source material" and "byproduct material" …

## Slide 3: TENORM Defined
Bottom Line
Naturally Occurring Radioactive Material
Concentrated
Human Activity
*Two Caveats*
Some would include materials not concentrated but rather relocated
Source Material, i.e. Uranium and Thorium are not included

## Slide 4: TENORM Generation
Water Treatment:
Drinking Water
  IX Media
  Green Sand
  HMO
  Soils from discharge area/impoundment
Wastewater (if there is a discharge to the system from another water treatment activity)
  Biosolids
  Drying beds
Industrial (any treatments that would likely concentrate metals)
  Any Filter media
  Soils from discharge area/impoundment

## Slide 5: TENORM Generation
O&G E&P:
Filter socks
Tank bottoms
Filter press cake
Residual materials dislodged during cleaning and maintenance activities on the following:
  Crude oil pipeline (pipe scale scraping/rattling/wire brushing)
  Natural Gas scrubbers, compressors, reflux pumps, control valves and product lines
  Gas/oil separators
  Dehydration vessels
  Liquid natural gas (LNG) storage tanks

## Slide 6: Regulatory Authority and Roles
Multiple regulating agencies:
  Solid Waste: Drinking water residuals, and solids going to commercial landfills, etc.
  Water Quality: Biosolids and front end of drinking water treatment, discharges to surface water, etc.
  Oil and Gas Commission: O&G Exploration and production activities
  Natural Resources: Mining activities
  Radioactive Waste Compacts: Movement
  State Radiation Control Programs: Protection
  Local Government: Certificates of Designation

## Slide 7: TENORM Disposal
Typical approaches:
  Concentration/Focus on safe long term disposal
  Treated as Solid Waste
  Radiological Dose And Risk Assessments for Municipal Solid Waste Landfill Disposal

## Slide 8: Risk Analysis / Radiological Dose Assessments
  Begins with identifying:
  The design and operational attributes of a facility
  The environmental conditions at the facility
  The radiological characteristics of the TENORM that is desired to be received
  The operational aspects of the facility: potential exposure routes

## Slide 9: Radiological Dose Assessments: Facility Design
Total airspace (total area and depth) of the facility/cell
Cover design
  Thickness, density, erosion rate
Engineered Liner/Barrier
  Thickness, density, hydraulic conductivity
Distance to groundwater
  Unsaturated layer
    Thickness, density, hydraulic conductivity
Methane gas collection system:
  Total gas production
  Flowrate of exhaust
  Dimensions of stack (height, diameter)

## Slide 10: Radiological Dose Assessments: Facility Environment
Climate/Weather Data:
  STAR data files
  Wind and precipitation data

## Slide 11: Radiological Dose Assessments: Facility Operations
Radiologic data:
  Isotopes and concentrations
Percent volume of TENORM waste
Daily Cover thickness
Identify Non-TENORM layers potentially at the bottom of the cell or the top of the cell prior to closure
Leachate collection and monitoring system
  Recirculation activities
Groundwater monitoring

## Slide 12: Radiological Dose Assessments: Models
RESRAD
  This is a computer code designed at Argonne National Laboratory for estimating radiation doses and cancer risks to an individual located on top of or near radioactively contaminated soils and to derive radionuclide soil guideline levels corresponding to a specific dose criterion
MILDOS-AREA
  The MILDOS-AREA computer code (MILDOS 4) is used to estimate the radiological impacts from airborne emissions from uranium milling facilities. This code may be used to estimate the Radiological dose from radon (Rn-222) to individuals who may be offsite but in the vicinity of the facility
CAP-88 PC
  The U.S. Environmental Protection Agency’s CAP-88 (Clean Air Act Assessment Package - 1988) computer model is a set of computer programs, databases and associated utility programs for estimating dose and risk from radionuclide emissions to air. This code may be used to estimate the Radiological dose from radon (Rn-222) to individuals who may be offsite but in the vicinity of the facility

## Slide 13: Radiological Dose Assessments: Models
Models must be run for the following scenarios:
Operational Phase
  Dose to worker during placement of TENORM materials (RESRAD-ONSITE)
  Dose to worker during placement of Non-TENORM materials (RESRAD-ONSITE)
Closure Phase
  Dose to offsite individuals from radon emissions through gas collection and evacuation system (MILDOS-AREA or CAP-88 PC)
Post Closure Phase
  Dose to a resident farmer out to 1000 years (RESRAD-ONSITE)

## Slide 14: Radiological Dose Assessments: Results
Establish Compliance Thresholds
25 mrem/year: Unrestricted Release
100 mrem/year: Public Limit for Licensed Activities
12 mrem/year or less: EPA and Risk vs Dose
Grant Approval to the Facility
Establish waste acceptance criteria
Require environmental covenant: Radon
Approve revised operations plans
Revise or obtain Certificate of Designation

## Slide 15: Challenges and Concerns
No Federal Regulatory structure
  States Issue
Public fears and the “R-word”
Labor intensive for site specific assessments
Costs to industry
Some materials are not suited for MSWLFs
A lot of cooks in the kitchen

## Slide 16: Overcoming the Challenges
Communicate with other states and national organizations
Ensure that assessments are clear and consistent
  Possible general assessments
Ensure that sampling, analysis, and characterization are consistent and defensible
Ensure that expectations of generators and disposal facilities are clear so that they can develop strategies to deal with the economic impacts
Clear communication and partnerships with all regulatory agencies

## Slide 17: Conclusions
TENORM is out there and it needs a home
Disposal options have to be established to avoid improper disposal
Well designed engineered Municipal Solid Waste Landfills can be a safe and protective disposal option

## Slide 18: Thank You For Your Time and Attention Questions?
http://www.colorado.gov/cdphe/
Jim Grice at james.grice@state.co.us or (303) 692-3371