## Slide 1
Site Overview
October 2024
David Carlson
President
865-201-3191
dcarlson@wcstexas.com

## Slide 2
Byproduct Facility

## Slide 3: WCS - Disposal Design (vs. Generic Facility)
  Key Attributes of WCS site:
  Sub-Grade Design
  Natural Claystone Barrier
  No viable pathway to groundwater
WCS Disposal
WCS is the Newest and Most Robust LLRW facility in the US
Other Facilities

## Slide 4: WCS - Compact Waste Facility (CWF)
Regulated by TCEQ (2 on-site inspectors)
Privately-developed and operated
Opened in 2012
Owned by the State of Texas

## Slide 5: Compact Waste Facility
Phase 2a – 15,000 cubie feet used
410,000 cubic feet available
Phase 1 - 360,000 cubic feet used
90,000 cubic feet available
Licensed – 9,000,000 cubic feet of disposal

## Slide 6: CWF Waste Disposal

## Slide 7: Cask Receipt

## Slide 8: Offloading a Cask
Liner (blue) is transferred from a transportation cask (grey) to a modular concrete container (MCC)
Liner is fabricated of steel and is bolted shut
Modular concrete container (MCC) is thick reinforced concrete
Lift from cask
Transfer
Lower into MCC

## Slide 9: Transfer MCC to Disposal

## Slide 10: MCCs in the Compact Waste Facility (CWF)

## Slide 11
Crystal River 3 (CR3)
Reactor Vessel Disposal

## Slide 12: Crystal River Unit 3 Reactor
Pressurized Water Reactor – B&W design
860 MW electrical capacity
Shutdown September 2009
Decommissioning started in October 2020

## Slide 13: CR3 – Reactor Sections
The reactor vessel was cut into 4 sections and packaged for transport
Mid Section is Class C low-level waste (LLW) and the other 3 sections are Class A LLW
Sections meet all NRC and DOT packaging requirements for transportation
 | Diameter (feet) | Height (feet) | Weight (tons)
Vessel Head | 17 | 8 | 95
Top Section | 19 | 13 | 370
Mid Section | 17 | 15 | 430
Bottom Section | 15 | 7 | 95

## Slide 14: CR3 Reactor Vessel - Transportation
Barge from Crystal River, FL to Aransas Pass, TX
Truck transport to WCS site in Andrews, TX

## Slide 15: CR3 Reactor Vessel – Barge Transport
Departed Crystal River January 22
Arrived Aransas Pass January 29

## Slide 16: CR3 Reactor Vessel – Road Transport
Top and Mid Sections configuration – 32 axle trailer (more than 250 wheels)
Shipments were all oversize and overweight
Routes and transportation parameters were predetermined by TXDOT
Avoids major roads and cities
Head and Bottom Section required about 4 days each (~700-mile route)
Top and Mid Sections required over 30 days each (~900-mile route)

## Slide 17: Transportation Challenges

## Slide 18: Arrival at WCS

## Slide 19: On-Site Transport

## Slide 20: Transport to Disposal

## Slide 21: Disposal Placement

## Slide 22: Final Disposal

## Slide 23: Thank You