## Slide 1
Waste Control Specialists
Spring 2025 - LLW Forum

## Slide 2: What We Do
Treatment of Hazardous and Mixed Waste
Logistics by Rail and Truck
On-site field services
  Characterization / Waste Planning
  Packaging / Shipping
Safe Disposal of Low-Level Radioactive Waste (LLRW)
  Class A/B/C LLRW and Mixed LLRW
  NORM, Oil & Gas NORM, and Byproduct material

## Slide 3: WCS Site – Relative Distances
Direct distance to communities:
Eunice, NM 5 miles
Hobbs, NM 15 miles
Jal, NM 24 miles
Andrews 30 miles
Seminole 30 miles
Odessa 50 miles
Midland 60 miles
WCS
Nearest residence is:
3.5 miles east, in NM @ 176 & 18
Nearest businesses are:
URENCO (uranium facility) - adjacent to site in NM
Lea County Landfill (trash disposal) - across 176 in NM
PB Materials (concrete plant) - NW site boundary in NM
Sundance Disposal (O&G waste) - NW site boundary in NM

## Slide 4
Compact
Facility
Federal
Facility
Hazardous
Waste
Landfill
Byproduct
Facility
Administration
Buildings
Treatment
Facilities
Rail
Offload
WCS Site – Facilities
14,000 acres (permitted area is 1,400 acres)
4 landfills, treatment facilities, rail access
Located on red-bed ridge

## Slide 5: WCS Environmental Protection (vs. Generic Facility)
  Key Attributes of WCS site:
  Sub-Grade Design
  Natural Claystone Barrier
  Thick Cover Design
  No viable pathway to groundwater
WCS Disposal
WCS is the Newest and Most Robust LLRW facility in the US
Other Facilities

## Slide 6: Extensive Subsurface Characterization
Over 640 wells/soil borings, numerous geologic/hydrologic investigations: 15 major geologic studies;
18 major hydrogeologic studies; 10 geophysical investigations.

## Slide 7: Performance Assessment
GoldSim-based modeling
Integrated PA for entire site examines:
  site geology
  surface water and groundwater
  potential future weather changes
  residential and intrusion scenarios
  possible future uses of the land
10,000-year compliance period, evaluated to one million (1,000,000) years
Majority of radionuclides have short half-life (Co-60, Fe-55, etc)
Some have longer half-life (C-14, N-63, U-238, Tc-99)
Current disposed inventory has a peak dose of 0.5 millirem per year - after >10,000 years

## Slide 8: Compact Waste Facility
Texas owned
Privately-developed and operated
Regulated by TCEQ (2 on-site inspectors)
Opened in 2012

## Slide 9: Federal Waste Facility
Federal government takes ownership post-closure
Privately-developed and operated
Regulated by TCEQ
Opened in 2013

## Slide 10: RCRA Subtitle C Landfill (Low Activity Waste)
Regulated by TCEQ
Privately-developed and operated
Opened in 1994
Accepts Exempt waste up to about
10% of the Class A limit

## Slide 11: WCS Transportation / Logistics

## Slide 12: Transportation Casks
The most modern and state-of-the-art casks in service
Provides protection of the public and the environment in the event of the most severe accident scenarios
Regulated by the Nuclear Regulatory Commission and the Department of Transportation
WCS-160 Type B casks – 3 units
WCS-215 Type A casks – 3 units (plus leases as needed)
WCS-160 Type B Cask
WCS-215 Type A Cask

## Slide 13: Cask Receipt

## Slide 14: Offloading a Liner from a Transportation Cask
Liner (blue) is fabricated of steel and is bolted shut
Liner is removed from the transportation cask (grey)
Liner is loaded into a reinforced concrete Modular Concrete Container (MCC)
Lift from cask
Transfer
Lower into MCC

## Slide 15: Transfer MCC to Disposal

## Slide 16: Irradiated Hardware Casks
WCS offloads TN-RAM, MP-197, 3-60B, WCS-160B
WCS routinely disposes of IH with dose rates >20,000 R/hr. on contact
Collective team dose is typically less than 0.02 person-rem
State-of-the-Art transfer system with complete remote handling
IH casks are routinely offloaded, reassembled and shipped back the same day

## Slide 17: Highway Transportation
2024 Highway Volume
  750 shipments
  4,000 containers
  600,000 cubic feet (25% of volume)

## Slide 18: Rail Access
Direct Rail:
Texas and New Mexico Railway (TXN) interchange to Union Pacific (UP) at Monahans
Transload to Truck:
Lubbock and Western Railway (LBWR) interchange to BNSF at Lubbock and transload
WCS has the infrastructure to support transportation of heavy loads
Rail lines upgraded to support shipments over 450,000 lbs
WCS

## Slide 19: Rail Transportation
WCS has has the only rail line in Andrews County
  Operates 3 locomotives
  4-mile rail loop encircles the licensed site
  5 miles of owned rail line from site to Eunice, NM
  Served by two Class 1 railroads (UP and BNSF)
2024 Rail Volume
  600 shipments
  5,000 containers
  3,000,000 cubic feet (75% of volume)

## Slide 20: WCS Waste Treatment/Processing LLRW, Mixed Waste, and Hazardous Waste

## Slide 21: Waste Storage
Covered storage (over 60,000 cubic feet):
  Container Storage Building - 36,750 cubic feet (5,000 - 55-gallon drum equivalents)
  Bin Storage Area - 17,118 cubic feet
  Stabilization Building - 8,000 cubic feet
Outdoor Storage:
  Bin Storage Units (BSU) - 87,480 cubic feet
  LSA Storage Pad – 1,500,000 cubic feet, 10-acres of area (radioactive only)
Waste Storage
RCRA/TSCA, Radioactive, and Mixed Waste

## Slide 22: Waste Treatment – Waste Types
Liquids, sludges, solids, lab packs in approved containers, and liquids in bulk tankers
Inorganic waste streams including acids, bases, and wastes contaminated with metals
Organic waste streams (with some concentration limitations)
High VOCs can be treated on a case-by-case basis
Water-reactive inorganic materials such as elemental lithium, sodium, etc.
Hazardous and non-hazardous wastes mixed with LLRW
Authorized Types of Waste
Container Storage Building

## Slide 23: Waste Treatment – Processes
Sorting and Segregation
Characterization (parent and daughter waste streams)
Decontamination
Repackaging
Volume Reduction
Chemical oxidation
Chemical reduction
Deactivation
Micro- and macro-encapsulation
Neutralization
Stabilization
Controlled reaction
Dewatering
Bulk Pan Treatment
Treatment Processes

## Slide 24: Treatment Facilities – MWTF
  Negative pressure, processing and treatment facility
  20,000 square feet of treatment space
  85-cubic-yard capacity mixing pan
  Isolated treatment room with a dedicated ventilation system within the MWTF and double containment (as necessary)
Mixed Waste Treatment Facility
Glove Box processing

## Slide 25: Treatment Facilities – Perma-Con
In 2023 WCS installed the largest Perma-Con in the U.S.
Supports preparation and shipment of LANL TRU waste
6500 sq. ft. floor space
HVAC/HEPA System
Remotely operated five (5) ton mobile gantry crane
Backup generator
Perma-Con

## Slide 26: Other Treatment and Storage Capabilities
Bulk Vitrification
Currently processing LLRW contaminated reactive metals
Plans in development for further complex and orphaned waste streams
Veolia GeoMelt

## Slide 27: DOE Problematic Waste Example
WCS Services
  Receipt and storage of waste
  Sorting and Segregation by:
    Physical Form
    Radiological Character
    RCRA and TSCA hazard profiles
Re-Packaged waste for most appropriate
  Treatment (as required)
  Disposal (according to radiological character of daughter waste streams)
Result
  Quicker removal from generating site
  Lower cost
  Burial according to actual radiological character
Waste Profile Included:
Class C debris and non-debris mixed waste requiring RCRA treatment.
Potentially included solidified and non-solid sludge, wood, metal, PPE, miscellaneous plastic and cellulosic material, drum bags, plastic bottles (with or without liquid), cardboard, paper, rags, batteries, absorbents, soil/sweepings,
Potential PCB contamination

## Slide 28: Depleted Uranium Disposal

## Slide 29: DOE Depleted Uranium (DU) Cylinders in Storage

## Slide 30: DOE DUF6 Conversion Plants – Portsmouth and Paducah
April 2025 Status | Paducah | Portsmouth | TOTAL | 
Total DU Cylinder Inventory | 43,000 | 19,000 | 62,000 | 
DUF6 Facility Size | 4 lines | 3 lines | 7 lines | 
DUF6 Facility Startup | 2011 | 2010 |  | 
Conversion/year (capacity) | 800 | 600 | 1,400 | 2%
Converted to date | ~5,500 | ~3,500 | ~9,000 | 15%
DOE DUF6 Facilities Convert DUF6 Tails to stable DUO2 for disposal
  DUF6 – depleted uranium hexafluoride (a gas when heated)
  Tails – the depleted and discarded portion after enrichment
  DUO2 – depleted uranium oxide (stable for disposal)
  Uranium Enrichment (increases fissionable U-235 percentage)
  Natural Uranium – 0.7% U-235 (99.3% U-238)
  Low Enriched Uranium (LEU) – 3% to 5% U-235
  Depleted Uranium (DU) – 0.2% to 0.3% U-235

## Slide 31: DUO2 Cylinder Disposal at WCS in Andrews, TX
DU Cylinders
4 feet diameter
12 feet long
28,000 lbs.

## Slide 32: WCS - Local Activities
Our Staff Lives in the Community
  Largest private employer in Andrews county
  Over 125 site employees, >$15 million payroll
  Employees are involved in the community
    (schools, chambers of commerce, churches, sports, etc.)
Local Engagement
  High School credit course and internships
  Outreach to Andrews and regional communities
  WCS office and staff presence in center of town
Financial Support
  Over $300 million invested in site and facilities
  Purchase of supplies and services from local companies
  Financial contributions to Community Activities
    Education Foundation
    Scholarships, Public Safety, Sports Teams, etc.
  Special Surcharges (5% of LLRW disposal revenue)
    Paid in addition to all normal taxes and fees
    Supports quality-of-life community improvements
    $20.4 million provided to Andrews County so far